## Slide 1: Concerns About the Potential for Induced Seismicity Associated with the Mississippian Play: Perceived or Real?
Austin Holland and Dr. G. Randy Keller
Oklahoma Geological Survey
University of Oklahoma

## Slide 2: Outline
Induced Seismicity Background
Induced Seismicity Regional Context
Potential for Induced Seismicity in the Mississippian Play
Possibilities for Risk Mitigation
Best Practices

## Slide 3: Earthquake Triggering
Natural Causes
Dynamically by the passage of seismic waves
  typically from very large earthquakes distances > 1000 miles
Statically by local stress changes from previous earthquakes
  Small amounts of stress changes have been shown to trigger earthquakes
  as little as 2-7 psi
Natural fluid movement
  May be the cause of many aftershocks of large earthquakes
Hydrologic loads
Anthropogenic
Reservoir Impoundment
Mining and Oil Production (Mass Removal)
Fluid Injection
Geothermal Production & Thermal Contraction

## Slide 4: Induced Seismicity from Fluid Injection
Most of the Earth’s upper crust is near failure
Increased pore pressure from fluid injection effectively reduces friction on fault
  Or in Mohr-Coulomb space moves the circle towards failure
σn
τ
τ
σn
Failure
τo
Add Pore Pressure
p
Notes: Size of the Mohr-Coulomb circles are the deviatoric stress sigma1-sigma3
Of course pressure doesn’t instantaneously increase as shown here, but how does it propogate within the Earth

## Slide 5: Pressure Diffuses Within the Earth
Pressure increase is not due to actual fluid flow
  Can be much more rapid
  Because water is fairly incompressible it is similar to an elastic response although slower
  Diffusivity is
    T = transmissivity
    S = storativity
Pressure increases over time
Talwani et al. (2007) J. Geophys Res.
Notes: Top figure shows the time progression of pressure from an injection well injecting at a constant pressure
Bottom figure shows the range of diffusivity observed in most cases of induced seismicity

## Slide 6: Risk from Induced Earthquakes
Hydraulic Fracturing (Lower Risk)
  Magnitudes less generally less than 0
  Observed maximum magnitude (Mmax) 3.1-3.4
  Injection duration may be weeks
Water Disposal (Higher Risk)
  Observed Mmax 5.3-5.7
  Damage from some events
  Injection duration may be decades
Notes: Generally seismol

## Slide 7
Magnitude
Courtesy of Art McGarr (USGS)
Injection Duration
RAT=Raton Basin
RMA=Rocky Mtn Arsenal.
YOH=Youngstown OH
PBN=Paradox Valley CO
GAK=Guy AK
BAS=Basel Switzerland
GAR=Garvin County OK
BUK=Bowland Shale UK
KTB=eastern Bavaria Germany
Notes: This plot of maximum seismic moment, the standard measure of earthquake deformation, as a function of total injected volume. Note that all of the large magnitude events are associated with wastewater disposal. The M3.4 earthquake in Basel Switzerland, although not very large, nonetheless had serious consequences, including project termination and many insurance claims. The maximum magnitude earthquakes in the Raton basin increased with total injection volume, M4.5 in 2001, M5 in 2005 and most recently, M5.3 in 2011. These data represent only the exceptionally large induced earthquakes. Indeed, the vast majority of injection wells do not produce earthquakes large enough to be felt by the public. For each point, wd=wastewater disposal, egs=enhanced geothermal system, and frak=hydraulic fracturing. RAT=Raton Basin, RMA=Rocky Mtn Arsenal. POH=Painesville OH, YOH=Youngstown OH, ASH=Ashtabula OH, PBN=Paradox Valley CO, GAK=Guy AK, CBN=Cooper Basin Australia, BAS=Basel Switzerland, STZ=Soutz sous Forets France, GAR=Garvin County OK, BUK=Bowland Shale UK, KTB=eastern Bavaria Germany.

## Slide 8: Injection Induced Seismicity
Best Documented Cases
Rangely, CO – Raleigh et al. (1976) Science
Paradox Valley, CO, Ake et al. (2005) Bull. Seismol. Soc. Amer.
KTB, Germany, Baisch et al. (2002) Bull. Seismol. Soc. Amer.
Basel, Switzerland, Deichmann & Giardini (2009) Seismol. Res. Letters
Rocky Mountain Arsenal, CO, Hsieh & Bredehoeft (1981) J. Geophys. Res.
General Observations
Earthquakes occur first near the well and migrate away from the well with time
Earthquakes have a clear temporal correlation to injection
Time and spatial distribution of earthquakes can generally be related to diffusion of pore pressure
Earthquakes can occur over long distances >20 km
Modifying injection parameters alters earthquake production

## Slide 9
RMA, Healy et al. (1968)
Rangely, Raleigh et al. (1976)
Paradox Valley, Ake et al. (2005)

## Slide 11: Induced Seismicity from Water Disposal
Possible Cases from Oklahoma
  M5.6 Prague Earthquake, 3 disposal wells within ~1 mile
  Jones Earthquake Swarm, ~1800 earthquakes, Mmax=4.0, large volume wells within 8-12 miles
  Examining other possible cases
Other recent possible cases
  Guy/Greenbrier, Arkansas, hundreds of earthquakes, Mmax=4.7
  Youngstown, Ohio, ~12 earthquakes, Mmax=4.0
  DFW Airport, Texas, ~11 earthquakes, Mmax=3.3
  Barnett Shale, Texas, 67-150 earthquakes, Mmax=3.0

## Slide 12: Outcome of recent cases
Voluntary or mandatory shut-in of UIC Class II disposal wells (Texas, Arkansas and Ohio)
Moratorium Zones for UIC Wells (Arkansas)
New permitting and monitoring requirements (Arkansas and Ohio)

## Slide 13: UIC Wells and Earthquakes
More than 7,500 active UIC Class II Wells in Oklahoma
Often spatially clustered

## Slide 14: Increase in Earthquakes Not Matched by Increase in Fluid Injection
Oklahoma Earthquakes
Chart: Oklahoma Injectors
| 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
# UIC II Injectors | 8721 | 9092 | 9862 | 10488 | 10656 | 10385 | 10055 | 10046 | 10092 | 10125 | 10342 | 10744 | 10770 | 10928

## Slide 15: Fluid Injection in Central, OK
Logan
Lincoln
Oklahoma
Pottawatomie

## Slide 16: Induced Seismicity from Hydraulic Fracturing
Recent Cases from Oklahoma
  Eola Field, Garvin County, ~100 earthquakes, Mmax=2.9
  Possible, Union City Field, Canadian County, ~10 earthquakes, Mmax=3.4
  Examining other possible cases
Other recent cases
  Blackpool, United Kingdom, >50 earthquakes, Mmax=2.3
  Horn River Basin, British Columbia, >40 earthquakes, Mmax=3.5

## Slide 17: Eola Field, Garvin County
Holland (2012) in review

## Slide 18
Holland (2012) in review

## Slide 19
psi>6000
Holland (2012) in review

## Slide 20: Union City Field, Canadian County
Straight Arrow Well
16 stage frac
  Completed 3/12 1:00 UTC
  First earthquake 3/11 07:41
  M3.4 at 23:57
  Total 10 earthquakes M2.1-3.4 on 3/11
Visually identify similar examples
Notes: The Straight Arrow well has a completion date in the OCC database of 2010-03-25.

## Slide 21: Induced Seismicity from Hydraulic Fracturing
Courtesy of Jim Rutledge
Garvin Co.
Notes: Bowland upper point is April stimulations stages 1 and 2, from
Bowland lower point is one month later, stages 4 and 5
OK point from Austin Holland’s updated magnitudes, volumes for stages 1 and 2.
Basel upper point is for 28 biggest events including three M3 within month of stimulation
Basel lower point is for pumping and immediate period afterwards.

## Slide 22: Maximum Magnitude
Earthquake magnitude is related to rupture area and the average slip over that area
Earthquake rupture dynamics
  Big earthquakes start small
Mmax controlled by
  fault size and properties
  stress on the fault
  initial rupture energy
t1
t2
t3
Large faults represent large potential hazards
knowing whether or not they are favorably oriented for slip is important
but to be cautious maybe greater set-backs are warranted

## Slide 23: Concerns of Induced Seismicity in the Mississippian Play
Significant amount of hydraulic fracturing
Large amounts of produced water to dispose of within the Arbuckle
Arbuckle is near the basement where faults may be stressed to near failure
  Fractures and faults in basement may be poorly if identified at all

## Slide 24: Avoiding Potentially Active Faults
154 earthquake focal mechanisms
Define the distribution of orientations for active faults in Oklahoma
This information can be used to modify operations to avoid faults
  oriented in a way that is more likely to have triggered earthquakes
  or are large, which may not be completely favorable to slip, but pose a greater hazard
Optimal Fault Orientations in Oklahoma
(in review Seismol. Res. Lett.)
T-axis
P-axis

## Slide 25: Calculate a Probability Density Function (PDF) from fault orientations
PDF for all earthquakes
Outside Jones Swarm
Example focal mechanisms
Prague M5.7 EQ Sequence

## Slide 26: Characterizing Fault Rupture Likelihood

## Slide 27: Risk Mitigation Strategies
Avoid injection into active or potentially active faults
Minimize and monitor pore pressure changes at depth
Install local seismic monitoring arrays
Establish modification protocols in advance
Be prepared to alter plans or abandon wells
Zoback (2012) Earth AGI

## Slide 28: OGS Seismic Station Sponsorship
Provides a way to transparently address the possibility of induced seismicity
Removes duplication between operators
Can be tailored to meet individual operators requirements
Rapid reporting for operational feedback for participants
Cost effective
Improves products like
  optimal fault orientations
  Earthquake locations
Equipment donations are tax deductible